## Slide 1: ASML DUV Stepper
Programming Worksheet
2022-11-08
Items in YELLOW must be filled in with your own values

## Slide 2: Wafer Layout
Cell Size: (X, Y) in mm
  This should include any dicing lanes/spacing between die.
Cell Shift: By default, Die # (0,0) is centered at (0,0)
  If you need to shift the entire Die matrix use Die Shift for this. Eg. a typical value might be ½ of the Die Size, so die corner falls on wafer center.
  (0, 0) mm – max is ½ of Die Size
 Example: 5mm die, shift=0,0 mm
Note the ASML’s coordinate system,
Col 0, Row 0 – is at center of the wafer.
(You can generate a schematic in Klayout)

## Slide 3: Mask Definition: Instructions
Which Parts of the Mask do you need exposed.
“Images” refer to individual pattern regions on the mask.
Example of 3 separate “Images” on the mask plate
Each Image needs (at 1x wafer-scale):
Image Center Coords
  w/r/to center of mask plate
Image Size
Name for this image (<10char., arbitrary)
Image Size: (3,3mm)
Image Center:
X
(4,5)mm
Image Name: “BOX3MM”
SEPARATE Slide for Each Mask Plate

## Slide 4: Mask Definition
Image/Layer ID | Image Size (wafer, mm) |  |  | Image Shift (wafer, mm) | 
 | X | Y |  | CenterX | CenterY
* Choose a short (<10char) name for each Image on your photomask, and enter the Size & Center coords for each Image. Add/delete rows as needed. |  |  |  |  | 
ImageName1 | 6.000000 | 3.900000 |  | -4.500000 | 0.000000
ImageName2 | 6.000000 | 3.900000 |  | -4.500000 | -5.000000
ImageName3 | 6.000000 | 3.900000 |  | -4.500000 | 5.000000
ImageName4 | 6.000000 | 3.900000 |  | 4.500000 | 5.000000
ImageName5 | 6.000000 | 3.900000 |  | 4.500000 | -5.000000
ImageName6 | 6.000000 | 3.900000 |  | 4.500000 | 0.000000
Please only include Images required for this specific exposure job.
Don’t include other images on mask that will not be used at this time.
Reticle Barcode: “UCSBJAN2020”
Make a SEPARATE Slide for Each Mask Plate

## Slide 5: Alignment Definition
Specify exact coordinates of alignment marks to be placed by the stepper, and type of Alignment mark.
Alignment Mark Locations: |  | (If Needed)
Mark Type | X | Y
PM | -38.5 | 10
PM | -38.5 | 0
PM | -38.5 | -10
PM | 38.5 | 10
PM | 38.5 | 10
PM | 38.5 | -10
Type of Mark (If an Image from previous slide, specify Image Name). System marks are: “PM” (std), “SPM-X”, “SPM-Y”
  These are all available on a system mask plate.

## Slide 6: Wafer Layout: Instructions
For each Image to be placed on the wafer, I need:
• Image name and which Die to fill.
• Acceptable to say “all”, or “all except: Row -1, Col 0” etc.
Note the ASML’s coordinate system,
Col 0, Row – is at center of the wafer.

## Slide 7: Wafer Layout
Image “BOX3MM”:
  Only Top half of wafer: Row 1 and UP to edge
Image “BOX4MM”
  Only BOTTOM half of wafer: Row 0 and DOWN to edge
  No images in Die: Row -5, Col 0 (Alignment marks)
  No Images in Die: Row +5, Col 0 (alignment marks)
CAD screenshot is welcome here to clarify any uncertainties